## Slide 1: ECE477 Midterm Design Review: Team 1
Notes: During the presentation make sure to introduce yourselves and identify your team roles.
Presentation Example 1: https://purdue.brightspace.com/d2l/le/dropbox/949519/947637/DownloadAttachment?fid=35974214
Presentation Example 2: https://purdue.brightspace.com/d2l/le/dropbox/949519/947637/DownloadAttachment?fid=35974216

## Slide 2: Outline
Project Overview
Major Components
Block Diagram
Packaging Design
Electrical Schematic (Microcontroller and Hardware)
PCB Layout (Microcontroller and Hardware)
Electrical Schematic (LED and Hall Effect System)
PCB Layout (LED and Hall Effect System)
Prototyping Progress
Software Development Status
Project Timeline
Questions
Notes: Grace

## Slide 3: Project Overview
An interactive game board that uses LEDs and Hall Effect (magnetic) sensors to simulate dungeon crawling games
Keeps user control and creativity but does the game calculations and character tracking automatically
Allows for user map building using a custom computer application sent to the game board through USB
Acts as a D&D "gaming console" for small groups
DUNgeon crawler board
Notes: Grace

## Slide 4: Project Overview
DUNgeon crawler board
LCD
Input Keypad
Hex Map
Notes: Grace

## Slide 5: PSDRs
PSDR #1 (Software): An ability to simulate a turn-based combat game involving pathing algorithms and object-oriented class systems.
PSDR #2 (Software): An ability to customize maps and characters on a computer via a Unity-based application.
PSDR #3 (Hardware): An ability to control rows of LED strips with DMA and PWM on microcontroller GPIO pins.
PSDR #4 (Hardware): An ability to control an array of Hall Effect sensors with I2C I/O expanders on a microcontroller.
PSDR #5 (Hardware): An ability to port information from a computer to a microcontroller via USB OTG.
Extra PSDR #1 (Hardware): An ability to store multiple preloaded maps on an SD card using SPI.
Extra PSDR #2 (Software): An ability to simulate ranged combat using line of sight algorithms, expanding the object-oriented class systems.
Main PSDRS and Stretch PSDRs
Notes: List your team’s PSDRs in this section. This slide is intended to be used for reviewer reference only, and should be passed over quickly during the actual presentation (as there are more important things to be discussed) Grace

## Slide 6: Major Components
Microcontroller
Hall Effect Sensors
I2C IO Expanders
LEDs
LCD
Keypad
Micro SD Reader
Buck Converter
Contents
Notes: Grace – I2C IO for Hall Effects

## Slide 7: Major Components
SELECTED: STM32F405VG
Microcontroller selection
Notes: Neil

## Slide 8: Major Components
Selected: AH9246-P-B
Digital
Operating Voltage: 2.5-5V
Average supply current: 8 µA
Alternative: SS49E
Analog
Operating Voltage: 4.5-6V
Average supply current: 4.2 mA
Hall Effect sensors
Notes: Landon

## Slide 9: Major Components
Selected: MCP23017
Operating Voltage: 2.8-5.5V
Low standby current: 1 µA max
16 bit remote Bidirectional I/O pins
Alternative: PCF8574
Operating supply voltage: 2.5-6V
Low standby current: 10 µA max
8 bit remote Bidirectional I/O pins
I2c IO Expanders
Notes: Landon

## Slide 10: Major Components
Selected: WS2812B
16 pins needed with PWM control
60mA max brightness all colors
Simple circuit design
Alternative: LED lamps
32 pins needed
60mA max brightness all colors
Matrix circuit design
Alternative 2: WS2812
Same specs as WS2812B but more complicated circuit design
LEDS
Notes: Landon

## Slide 11: Major Components
Selected: ILI9341
Average voltage: 1.65-3.3V
Average current: 1μA
Protocol: SPI
Size: 2.2 in
Resolution: 240x320
Alternative: CFAF320480C7-035TN
Average voltage: 1.65-3.3V
Average current: 8mA
Protocol: SPI
Size: 2.2 in
Resolution: 240x320
LCD SCREEN
Notes: Jackson

## Slide 12: Major Components
Selected: Adafruit Standard 4x4
Max Voltage: 24V
Price: $5.95
Buttons: 16
GPIO Pins: 8
Alternative: Parallax Membrane 4x4
Max Voltage: 24V
Price: $9.95
Buttons: 16
GPIO Pins: 8
Keypad
Notes: Jackson

## Slide 13: Major Components
Selected: MSD 1-A
Max Voltage: 30V
Current: 0.5A
Pins: 9
Price: $0.23
SD 2.0
Alternative: MSD4-1-A
Max Voltage: 30V
Current: 0.5A
Pins: 9
Price: $2.50
SD 4.0
Micro SD Reader
Notes: Grace

## Slide 14: Major Components
Selected: Pololu 3.3V, 500mA Step-Down Voltage Regulator
Voltage Range: 3.4V - 36V
Pins: 4
Output Current: 500mA
Price: $5.95
Alternative: AMS1117-3.3 DC 4.75V-12V to 3.3V Voltage Regulator
Voltage Range: 4.75V-12V
Pins: 3
Output Current: 800mA
Price: $6.99
Buck converter
Notes: Neil

## Slide 15: Block Diagram
Electrical Diagram
Notes: Neil

## Slide 16: Packaging Design
Board Design
Notes: Jackson

## Slide 17: Packaging Design
Board Design - Materials
Notes: Jackson

## Slide 18: Electrical Schematic
MICROCONTROLLER AND Hardware
Notes: Jackson

## Slide 19: Electrical Schematic
Microcontroller
Notes: Jackson

## Slide 20: Electrical Schematic
Reset, Boot, and Clock
Notes: Jackson

## Slide 21: ElectRical Schematic
ST-Link
Notes: Jackson

## Slide 22: ELectrical Schematic
Power
Notes: Jackson

## Slide 23: Electrical Schematic
USB
Notes: Jackson

## Slide 24: Electrical Schematic
Micro SD Reader
Notes: Jackson

## Slide 25: Electrical Schematic
Keypad
Notes: Jackson

## Slide 26: Electrical Schematic
LCD
Notes: Jackson

## Slide 27: Electrical Schematic
Connectors to Hex Array PCBs
Notes: Jackson

## Slide 28: PCB Layout
Microcontroller and Hardware
Length: 112 mm
Width: 72 mm
Notes: Jackson

## Slide 29: PCB Layout
Microcontroller
Notes: Jackson

## Slide 30: PCB Layout
Power and USB
Notes: Jackson

## Slide 31: PCB Layout
Micro SD Reader
Notes: Jackson

## Slide 32: PCB Layout
ST-Link and Reset
Notes: Jackson

## Slide 33: PCB Layout
Keypad, LCD, and Connector to Hex Array PCBs
Notes: Jackson

## Slide 34: 3D View
Microcontroller and Hardware
Notes: Jackson

## Slide 35: FOotprint Verification
MicroContorller and Hardware
Notes: Jackson

## Slide 36: Electrical Schematic
LED and Hall effect system
Notes: Landon

## Slide 37: ELECTRICAL SCHEMATIC
WS2812B
Notes: Landon

## Slide 38: ELECTRICAL SCHEMATIC
IO Expander to Hall Effect Sensors
Notes: Landon

## Slide 39: ELECTRICAL SCHEMATIC
IO EXPANDER ADDRESS PINS
Notes: Landon

## Slide 40: PCB Layout
LED and Hall effect system
Length: 450 mm
Width: 25 mm
Notes: Landon

## Slide 41: PCB Layout
Front End Connectors & IO Expander to LEDS and SENSORS
Notes: Landon

## Slide 42: PCB Layout
WS2812B w/Decoupling capacitor
Notes: Landon

## Slide 43: PCB Layout
WS2812B w/Decoupling capacitor
Data Line
GND
5V Supply
Notes: Landon

## Slide 44: PCB Layout
HALL EFFECT Sensor placement
Hall effect spacing measurement
Notes: Landon

## Slide 45: PCB Layout
IO expander to Hall effects sensors
IO Expander GPIO Port to first sensor
Notes: Landon

## Slide 46: PCB Layout
16 board power system
5V Supply
GND Supply
3.3V Supply
Notes: Landon

## Slide 47: PCB Layout
I2C Control
I2C SCL
I2C SDA
Notes: Landon

## Slide 48: PCB Layout
WS2812B Data Line In
WS2812B Data Line
Notes: Landon

## Slide 49: PCB Layout
IO expander address setting
IO Expander Address Pins set with 0 Ohm resistors
Notes: Landon

## Slide 50: 3D View
WS2812B & Hall effect system
Notes: Landon

## Slide 51: FOotprint Verification
WS2812B & HALL EFFECt SYSTEM
Notes: Landon

## Slide 52: Prototyping Progress
WS2812B control using PWM - Completed
  24-bit color signals to each pixel
I2C Control - Completed
  Multiple addressable MCP23017 slave devices reading hall effect sensors
WS2812B & HALL EFFECt SYSTEM
Notes: Landon

## Slide 53: Prototyping Progress
USB OTG
  Able to receive data from computer in a buffer to be loaded into the program
SD Card
  Able to recognize MicroSD card and send and receive data using SPI
LCD
  Displayed text on LCD using STM32F091
Keypad
  Received keypad input using an STM32F091
User INterface
Notes: Neil

## Slide 54: Software Development Status
Overview
Not Started
In Progress
Completed
Notes: Grace [Insert Keypad]

## Slide 55: Software Development Status
General I/O & Import/Storage
Notes: Grace

## Slide 56: Software Development Status
General I/O
Notes: Grace

## Slide 57: Software Development Status
Computer Application – Overview
Page 1: Map Creation
Users can select a hex type and assign it to the map
Types: Floor, Wall, Character, Enemy, and Chest
Page 2: Character Creation
Users can input their character's name, class, and stats
Export to Microcontroller
Maps and characters are translated into a text file for export
USB receives text file through USB-OTG
Notes: Grace

## Slide 58: Software Development Status
Computer Application – Main Page View
Hex Type Selection
Export as Text File
16x16 Hex Map
Hex Selection
Notes: Grace

## Slide 59: Software Development Status
Computer Application
Notes: Grace

## Slide 60: Software Development Status
Gameplay – General Overview
Initialization
Receives game input from USB communication
Map data stored array of hexagon objects
Character data stored in priority queue of character objects
Movement
Moves players efficiently using A* algorithm
Updates map after a player confirms move
Combat
Determines which character will prevail in combat based on a combination of character statistics
Remove a character from map and turn order when out of health
Notes: Neil

## Slide 61: SOFTware development status
Gameplay – general overview
Specific character types and hexagon types inherit from a main class
GameCharacter and GameMap classes contain data structures that hold their respective objects
Notes: Neil

## Slide 62: Software Development Status
Gameplay – Important Classes and Structs
Notes: Neil

## Slide 63: Software Development Status
Gameplay – Hexagon Map
Notes: Neil

## Slide 64: Software Development Status
Gameplay
Notes: Neil

## Slide 65: Project Timeline
GANTT CHart
Notes: Neil

## Slide 66: 3D Printing
Questions?
Notes: Grace: 12 Neil: 10
Landon: 20 Jackson: 22