## Slide 1: ECE 477 Final Review: Team # 1

## Slide 2: Outline
Project Overview
Block Diagram
Design Challenges
Individual Contributions
Project Video Demonstration
Questions

## Slide 3: Project Overview
The Dungeon Crawler is an interactive electronic game board used to customize and simulate dungeon crawling games
Laptop application is used to design the map and characters, and the USB ports info to board
Game board utilizes pixels and Hall Effect (magnetic) sensors to display map and track characters
LCD and keypad display prompts and receive inputs for gameplay
Acts as a D&D "gaming console" for small groups

## Slide 4: PROJECT OVERVIEW

## Slide 5: Block Diagram

## Slide 6: Design Challenges
WS2812B Pixels
  Timer and DMA conflicts
  Floating voltages in data line
17 PCBs to solder, with over 1000 components altogether
  Several connections between boards, multiplying potential problems
Mechanical Design Constraints
  Fitting PCBs, hex dividers, and plastic top
Weak solder connection on USB port
Application
  Inconsistency in exporting characters and map
  Designing Unity UI to be user-friendly
Paradoxical acrylic glue

## Slide 7: Individual contributions
WS2812B and I2C I/O Expanders
  Prototyped lighting in series
  Prototyped I2C communication to multiple addressed MCP23017s
LED and Hall Effect Sensor PCB Design
Soldering/PCB Manufacturing
  Soldered components and ran system design checks on completed boards
Gameplay Code Contributions
  Focused on the movement, combat, and chests
Final Packaging
  Helped insert PCBs and other components into wooden frame
Landon Carre

## Slide 8: Individual contributions
USB Protocol
  Developed USB OTG protocol
  Designed circuit for USB
Tested and extended previously written software
Soldered PCBs
  Hot plated gameplay PCBs, hand soldered USB and SD reader to main PCB
Gameplay Code
  Created game loop state that controls player turns
  Helped with line of sight and FOV algorithms
Final Packaging
  Created holes for power and USB connectors, data lines for LCD and keypad
Neil Brown

## Slide 9: Individual contributions
Software Outline
  Developed object-oriented structure and pathing algorithms
Prototyped Components
  Focused on LCD and keypad, helped with Hall Effect sensors
Designed, soldered, and debugged most of main PCB, helped with the other 16 PCBs
Final Packaging
  Designed container and found manufacturer
Software Outline (Again)
  Wrote portion of software flowchart, outlined state machine format
Developed Firmware
  Helper functions for LCD, interrupts for keypad
Debugging Game Logic
  Focused on FOV and ranged combat, contributed to initialization of monsters
Jackson Luna-McCrocklin

## Slide 10: Individual contributions
Companion Application
  Designed interactive UI for map and character editing
  Parsed and exported map and character information via USB
Prototyping
  Focused on MicroSD reader, helped with USB OTG
PCB Assembly
  Hot plated and hand soldered components on the 16 gameplay PCBs
Final Packaging
  3D modeled and printed hex dividers to go underneath acrylic display
  Cut plywood and acrylic top for playing area
Filled out remainder of the software flowchart and debugged gameplay code
Grace Whitaker

## Slide 11: Project Demonstration
PSDR #1 (Software): An ability to simulate a turn-based combat game involving pathing algorithms and object-oriented class systems.
PSDR #2 (Software): An ability to customize maps and characters on a computer via a Unity-based application.
PSDR #3 (Hardware): An ability to control rows of LED strips with DMA and PWM on microcontroller GPIO pins.
PSDR #4 (Hardware): An ability to control an array of Hall Effect sensors with I2C I/O expanders on a microcontroller.
PSDR #5 (Hardware): An ability to port information from a computer to a microcontroller via USB OTG.

## Slide 12: Project Demonstration VIDEO
https://youtu.be/Y_AnHLYayX4

## Slide 13
Questions?